Universal Injector Test Kit

User Manual

This test kit drivers all kinds of gasoline/diesel injectors, including PFI/ FSI/ TFSI/ GDI/ Peizo etc. it detects the type of injector automatically and works with a single button click.

The kit also provides common adapters for most Direct Injection injectors to fit in the fuel rails of most traditional PFI injector testers, for testing the injectors’ spray-ability.

● Specifications

| Power supply: DC12V | Operating temperature: - 20 ~ 60oC |
| --- | --- |
| Current: 1Amp | Humidity: <85% |

● Packing List

| 01 Driverbox 01 AC/DC Adapter | 01 Power Cord 01 Signal Output Cord |
| --- | --- |
| 06 Fitting Adapters | 01 Extension Cord |

|  | ● Structure of the Driverbox ① Signal Output Port ② 12V Power Supply Introduction Port ③ Decrease Button ④ Increase Button ⑤ Start/Stop Button ⑥ Power Indication LED ⑦ Coil type Injector Indication LED ⑧ Peizo Injector Indication LED ⑨ Output Signal Indication |
| --- | --- |

● Driverbox Operation Instruction

- Introduce 12V vehicle battery power supply or DC12V switch power supply to ②12V Power Supply Introduction Port,⑥Power Indication LED will be ON.

- Plug the signal output cord into the①Signal Output Port, and another endto the injector, the Driverbox would automatically detect the type of injector (peizo or peak&hold) in a few seconds, and the light the LED in accordance. if it failed to tell the right type of injector, check the connection or use a meter to test if the resistance of the injector is improper(injector faulty).

- Press⑤Start/Stop Button,the driverbox will start to output signal, and the injector would trigger ‘click’ sound otherwise the injector is faulty, the initial interval is 1Hz.

- Press ④Increase Button, the speed would increase from 1Hz to 3/5/10/20Hz, and press ③Decrease Button to slow it down.

- Press ⑤Start/Stop Button again to stop signal output.

● Adapters

There are 6pcs of adapters for fitting different injectors to a fuel rail of a traditional PFI gasoline injector tester.

| Shape | Specification | Usage |
| --- | --- | --- |
|  | Φ6 to G1/4 | Fitting for the fuel introduction port of Bosch Peizo injector, eg., the injector in some Mecedes-Benz. |
|  | Φ11.5 with O-ring to G1/4 | Fitting for round-shaped injectors like those applied on BMW B38/48. |
|  | Φ11.5 to G1/4 | Fitting for VW or other injectors with O-ring |
|  | M12x1.5 to G1/4 | Fitting for injector with M12 fuel introduction port like BMW or others |
|  | G1/4 to M12x1.75 | For convert G1/4 thread to M12x1.75, which was the standard of fuel rail of PFI injector tester made by some other manufacturers |
|  | Φ16 to Φ8.5 | Fitting for smaller type of injectors which might not be big enough to fit into the rack on the top of the injector tester. |

* Fittings for some other types of injectors might could be found within the standard PFI injector tester’s accessories.

*Latest fittings released, may not shown in this manual.

● Usage of the Fittings on a regular injector tester

Take the peizo injector graph on the left for reference,

- Apply the Φ6 to G1/4 adapter on the fuel introduction port.

- Apply the Φ16toΦ8.5 adapter at the bottom part of the injector and mount it onto the fuel rail of PFI injector tester then lock it good.

- Run the Leakage Test function on the PFI injector tester.

4. Connect the Driverbox and test the spray-ability of the injector.

● Usage of the Fittings on a high pressure diesel pump

Hand pump could be used as pressure source for test the injectors, diesel is recommended to test all injectors including gasoline.

Only injector with thread fitting is allowed to test with hand pump.

- Pressure up the hand pump to desired pressure, and check the sealing of the nozzle.

- Connect the Driverbox and test the spray-ability of the injector.

● Warranty

- The driverbox main unit entitled free warranty since the date of purchasing up to 12 months.

- For warranty issue concerning the accessories, please make inquiry to the distributor.

- Any damage to the device caused by misuse, or improper operation, is not covered by warranty.